## Slide 1: Compressor-Performance-Analyzer
The Compressor Performance Analyzer is a sophisticated, browser-based thermodynamic simulation platform designed to help engineers, researchers, and students accurately analyze, optimize, and forecast the performance of multi-stage centrifugal air compressor systems.

## Slide 2
CH3
CH3
302
+
COOH
COOH
2H2O
+
CH3
CH3
02
+
CH3
CHO
H2O
+
CH3
CHO
0.502
+
CH3
COOH
CH3
COOH
02
+
CHO
COOH
H2O
+
Step vise Reaction :
4-Methyl Benzaldehyde
Para Toluic Acid
4-Carboxy Benzaldehyde
HBR,CO/MN Acetate in Acidic Medium
200 C, 14.7(Barg)
CHO
COOH
0.502
+
COOH
COOH
Terepthalic Acid
Reaction Pathway for PTA Production From Para-Xylene
Process Air Compressor (PAC) - Process Description
+
Heat
  Atmospheric air enters the compressor through the inlet section.
  Air is compressed in five stages.
  The pressure increases progressively in each stage.
  Compression increases air temperature.
  Intercoolers remove heat between stages.
  Compressed air leaves the fifth stage at the required process pressure and temperature.
  The compressed air is then supplied to downstream process units.
Working Principle
Overall Reaction:
1
Configuration of PAC
  Five-stage centrifugal compressor.
  Intercooler between 1st and 2nd stage.
  Intercooler between 2nd and 3rd stage.
  Intercooler between 3rd and 4th stage.
  Steam Turbine, Process Air Compressor, and Expander are mounted on a common shaft.
  Inlet Guide Vanes (IGV) provided for flow control.
  During start-up, the compressor is driven by an electric motor.
  During normal operation, the compressor is driven by a steam turbine and expander.
  Integrated turbine-expander arrangement enables energy recovery and utilization.
  This arrangement improves plant energy efficiency.
Compressor Drive System

## Slide 5
Comparison of Rated and Calculated Compressor Performance Data :
Stage | Pin (bar a) | Pout (bar a) | Tin (C) | Tout (C)
1st | 0.99 | 2.319 | 45 | 145
2nd | 2.319 | 4.45 | 40 | 120
3rd | 4.43 | 8.19 | 39 | 105
4th | 8.19 | 12.25 | 39 | 107
5th | 12.25 | 18.3 | 107 | 153
Stage | Kin | Kout | Zin | Zout
1st | 1.398 | 1.3938 | .9996 | 1.0003
2nd | 1.4009 | 1.3978 | .9993 | 1.0012
3rd | 1.4059 | 1.4043 | .9988 | 1.0007
4th | 1.4107 | 1.4099 | .9984 | 1.0012
5th | 1.4099 | 1.4081 | 1.0012 | 1.0041
Design
Calculated
Stage | Pin (bar a) | Pout (bar a) | Tin (C) | Tout (C)
1st | 0.9932 | 2.34 | 34 | 138.3
2nd | 2.3432 | 4.44 | 55.8 | 140.8
3rd | 4.4432 | 7.3532 | 39.9 | 107.9
4th | 7.3532 | 12.3932 | 43.8 | 106.8
5th | 13.05 | 18.3 | 106.8 | 153
Stage | Kin | Kout | Zin | Zout
1st | 1.398 | 1.3938 | .9996 | 1.0003
2nd | 1.4009 | 1.3978 | .9993 | 1.0012
3rd | 1.4059 | 1.4043 | .9988 | 1.0007
4th | 1.4107 | 1.4099 | .9984 | 1.0012
5th | 1.4099 | 1.4081 | 1.0012 | 1.0041

## Slide 6
App Screenshot

## Slide 7
Comparison of Design and Calculated Inlet Air Conditions :
Relative Humidity | 60 | %
Atomspheric Pressure | 0.99 | bar
Suction Pressure | 99000 | Pa
Temperaturein | 45 | C
Vapour Pressure of Water Vapour | 9552 | Pa
Partial Pressure of Water Vapour | 5731 | Pa
Mole Fraction(Xw) of water in | 0.05789 | 
Relative Humidity | 65 | %
Atomspheric Pressure | 0.9932 | bar
Suction Pressure | 99320 | Pa
Temperaturein | 34 | C
Vapour Pressure of Water Vapour | 5302 | Pa
Partial Pressure of Water Vapour | 3446 | Pa
Mole Fraction(Xw) of water in | 0.03470 | 
Design
Calculated

## Slide 8
Stage | Xwin | Pin | Tin | Pstageout | Tstageout | Pcoolerstage,out | Tcoolerstage,out | V.Pstage out | Xwout | Remarks
1 | 0.05789 | 0.99 | 45 | 2.32 | 145 | 2.319 | 40 | 7352.789 | 0.03171 | Condensation
2 | 0.03171 | 2.319 | 40 | 4.43 | 120 | 4.43 | 39 | 6969.77 | .01573 | Condensation
3 | 0.01573 | 4.43 | 39 | 8.19 | 105 | 7.81 | 50 | 12296.2 | .01501 | Condensation
4 | 0.01501 | 8.19 | 50 | 12.25 | 107 | 12.25 | 107 | 129570.3 | .01501 | No Condensation
5 | 0.01501 | 13.05 | 107 | 18.3 | 153 | 18.3 | 153 | 511403 | .01501 | No Condensation
Stage-wise Water Vapour Mole Fraction Analysis (Design Case) :
Design

## Slide 9
App Screenshot

## Slide 10
Stage-wise Water Vapour Mole Fraction Analysis (Calculated Case) :
Calculated
Stage | Xw,in | P,in | T,in | Pstageout | Tstageout | Pcoolerstage,out | Tcoolerstage,out | VP stage out | Xw,out | Remarks
1 | 0.03470 | 0.9932 | 34 | 2.34 | 138.3 | 2.3432 | 55.8 | 16301.2 | 0.03470 | No Condensation
2 | 0.03470 | 2.3432 | 55.8 | 4.44 | 140.8 | 4.4432 | 39.9 | 7313.687 | 0.01646 | Condensation
3 | 0.01646 | 4.4432 | 39.9 | 7.3532 | 107.9 | 7.81 | 43.8 | 8978.649 | 0.01221 | Condensation
4 | 0.01221 | 7.3532 | 43.8 | 12.3932 | 106.8 | 12.3932 | 106.8 | 128698.1 | 0.01221 | No Condensation
5 | 0.01221 | 13.05 | 106.8 | 18.3 | 153 | 18.3 | 153 | 511403.4 | .01221 | No Condensation

## Slide 11
App Screenshot

## Slide 12
Stage | Xw,in | Xw,out | Remarks | Water In (kmol/hr) | Water Out (kmol/hr) | Water Condensed (kg/hr)
1 | 0.05789 | 0.03171 | Condensation | 1039.725 | 554.026 | 8742.6
2 | 0.03171 | .01573 | Condensation | 554.026 | 270.451 | 5104.4
3 | 0.01573 | .01501 | Condensation | 270.451 | 257.895 | 226.0
4 | 0.01501 | .01501 | No Condensation | 257.895 | 257.895 | 0.0
5 | 0.01501 | .01501 | No Condensation | 257.895 | 257.895 | 0.0
Design Case - Stage-wise Water Condensation :
Design

## Slide 13
Mw of water from 5th stage discharge | 28.80264542 | g/mol | -- | --
Moles of Wet Air | 17959.16229 | Kmole/hr | 510.0402 | t/hr
moles of dry air | 16919.43686 | kmole/hr | 480.512 | t/hr
Mass of water in air at suction condition | --- | --- | 29.5282 | t/hr
Comparison of Mass of Water in Air at Suction Condition (Design vs. Calculated) :
Mw of water from 5th stage discharge | 28.8333313 | g/mol | -- | --
Moles of Wet Air | 18662.46449 | Kmole/hr | 530.014 | t/hr
moles of dry air | 18014.88983 | kmole/hr | 511.6229 | t/hr
Mass of water in air at suction condition | --- | --- | 18.39113 | t/hr
Design
Calculated

## Slide 14
Calculated Case - Stage-wise Water Condensation :
Calculated
Stage | Xw,in | Xw,out | Remarks | Water In (kmol/hr) | Water Out (kmol/hr) | Water Condensed (kg/hr)
1 | 0.03470 | 0.03470 | No Condensation | 647.575 | 647.575 | 0.0
2 | 0.03470 | 0.01646 | Condensation | 647.575 | 301.495 | 6229.4
3 | 0.01646 | 0.01221 | Condensation | 301.495 | 222.691 | 1418.5
4 | 0.01221 | 0.01221 | No Condensation | 222.691 | 222.691 | 0.0
5 | 0.01221 | .01221 | No Condensation | 222.691 | 222.691 | 0.0

## Slide 15
Comparison of Stage-wise Water Condensation Across Intercoolers (Design vs. Calculated) :
Result Of all 5 stages :
Condensation in 1st stage(E-116) | 8.75 | t/hr
Condensation in 2nd stage(E-117) | 5.11 | t/hr
Condensation in 3rd stage(E-118) | 0.23 | t/hr
Total Water Condensed | 14.0886 | t/hr
Remaining Water in air | 15.4 | t/hr
Total Remaining air Flow | 496.0 | t/hr
Result Of all 5 stages :
Design
Calculated
Condensation in 1st stage(E-116) | 0.00 | t/hr
Condensation in 2nd stage(E-117) | 6.24 | t/hr
Condensation in 3rd stage(E-118) | 1.42 | t/hr
Total Water Condensed | 7.6564 | t/hr
Remaining Water in air | 10.7 | t/hr
Total Remaining air Flow | 522.4 | t/hr

## Slide 16
Stage-wise Compressor Efficiency Analysis (Design Case) :
Result Of all 5 stages :
Design
Stage | Efficiency(%) | Kavg. | Pout/Pin | (K-1)/K | Tout/Tin | Zout/Zin
1 | 88.1 | 1.396 | 2.342 | 0.284 | 1.314 | 0.99685
2 | 80.5 | 1.39935 | 1.910 | 0.285 | 1.256 | 1.00190
3 | 84.4 | 1.4051 | 1.763 | 0.288 | 1.212 | 1.00190
4 | 82.0 | 1.4103 | 1.593 | 0.291 | 1.176 | 1.00280
5 | 83.8 | 1.4090 | 1.402 | 0.290 | 1.121 | 1.00290

## Slide 17
Stage-wise Compressor Efficiency Analysis (Calculated Case) :
Result Of all 5 stages :
Calculated
Stage | Kavg. | Pout/Pin | (K-1)/K | Tout/Tin | Zout/Zin | Efficiency(%)
1 | 1.396 | 2.359 | 0.284 | 1.340 | 0.99685 | 84.2
2 | 1.39935 | 1.896 | 0.285 | 1.256 | 1.00190 | 78.8
3 | 1.4051 | 1.758 | 0.288 | 1.217 | 1.00190 | 81.9
4 | 1.4103 | 1.685 | 0.291 | 1.199 | 1.00280 | 82.5
5 | 1.4090 | 1.402 | 0.290 | 1.22 | 1.00290 | 83.4

## Slide 18
App Screenshot

## Slide 19
App Screenshot

## Slide 20
Stage-wise Polytropic and Actual Power Analysis (Design Case) :
Result Of all 5 stages :
Design
Stage | Actual Power(MW) | Polytopic Power(KW) | Polytropic exponent, n | n/(n-1) | Mw inlet | Zin | Tin(K) | AirFlow(Kg/s)
1 | 14.43 | 12891 | 1.4665 | 3.149 | 28.33 | 0.9996 | 318.15 | 141.34
2 | 11.42 | 9188 | 1.549 | 2.820 | 28.62 | 0.9993 | 313.15 | 138.91
3 | 9.18 | 7744 | 1.519 | 2.926 | 28.79 | 0.9988 | 312.15 | 137.49
4 | 7.91 | 6484 | 1.550 | 2.818 | 28.80 | 0.9984 | 323.15 | 137.43
5 | 6.47 | 5416 | 1.530 | 2.886 | 28.80 | 1.0012 | 380.15 | 137.43

## Slide 21
Stage-wise Polytropic and Actual Power Analysis (Calculated Case) :
Result Of all 5 stages :
Calculated
Stage | Polytropic exponent, n | n/(n-1) | Mw inlet | Zin | Tin(K) | AirFlow(Kg/s) | Polytopic Power(KW) | Actual Power(MW)
1 | 1.508 | 2.967 | 28.59 | 0.9996 | 307.15 | 148.20 | 13172 | 15.65
2 | 1.568 | 2.760 | 28.59 | 0.9993 | 328.95 | 148.20 | 10202 | 12.95
3 | 1.543 | 2.841 | 28.79 | 0.9988 | 313.05 | 146.46 | 8252 | 10.08
4 | 1.545 | 2.834 | 28.83 | 0.9984 | 316.95 | 146.07 | 7639 | 9.26
5 | 1.534 | 2.873 | 28.83 | 1.0012 | 379.95 | 146.07 | 5749 | 6.89

## Slide 22
Findings :
Stage | Efficiency Observation | Result | Conclusion
1 | Design: 88.1% Actual: 84.2% | 3.9% efficiency reduction. | Highest performance deterioration; priority for improvement.
2 | Design: 80.5% Actual: 78.8% | 1.7% efficiency reduction. | Indicates higher thermodynamic losses and requires performance optimization.
3 | Design: 84.4% Actual: 81.9% | 2.5% efficiency reduction. | Moderate performance deterioration.
4 | Design: 82.0% Actual: 82.5% | 0.5% efficiency improvement | Operating close to design conditions.
5 | Design: 83.8% Actual: 83.4% | 0.4% efficiency reduction. | Stable compressor performance.
Overall PAC | Design: 83.76% Actual: 82.16% | 1.6% overall efficiency reduction. | Performance degradation is mainly concentrated in Stages 1–3.

## Slide 23
Result of all the table :
Result Of all 5 stages :
Result Of all 5 stages :
Design
Calculated
Stage | Air Flow(kg/s) | Actual power (MW) | Efficiency | Water condensation (Kg/hr) | Polytropic power(KW)
1 | 141.34 | 14.67 | 88.1 | 8742.6 | 12917
2 | 138.91 | 11.42 | 80.5 | 5104.4 | 9188
3 | 137.49 | 9.18 | 84.4 | 226.00 | 7744
4 | 137.43 | 7.91 | 82.0 | 0.0 | 6484
5 | 137.43 | 6.47 | 83.8 | 0.0 | 5416
Stage | Water condensation | Air Flow(kg/s) | Polytropic power(KW) | Actual power (MW) | Efficiency
1 | 0.0 | 148.20 | 13172 | 15.65 | 84.2
2 | 6229.4 | 148.20 | 10202 | 12.95 | 78.8
3 | 1418.5 | 146.46 | 8252 | 10.08 | 81.9
4 | 0.0 | 146.07 | 7639 | 9.26 | 82.5
5 | 0.0 | 146.07 | 5749 | 6.89 | 83.4

## Slide 24
Result of all stage water condensation :
Water condensed in 1st stage | 0.0 | kg/hr
Water condensed in 2nd stage | 6229.4 | kg/hr
Water condensed in 3rd stage | 1418.5 | kg/hr
Water condensed in 4th stage | 0.0 | kg/hr
Water condensed in 5th stage | 0.0 | kg/hr
Result Of all 5 stages :
Water condensed in 1st stage | 8742.6 | kg/hr
Water condensed in 2nd stage | 5104.4 | kg/hr
Water condensed in 3rd stage | 226.00 | kg/hr
Water condensed in 4th stage | 0.0 | kg/hr
Water condensed in 5th stage | 0.0 | kg/hr
Result Of all 5 stages :
Design
Calculated

## Slide 25
Future Plans
  Shell-Side and Tube-Side Heat Balance Evaluation of intercoller.
  Determination of the Polytropic Exponent of the PAC Compressor in PTA-5/6.
  Polytropic Power Calculation of the PAC Compressor in PTA-5/6.
  Actual Power Consumption Analysis of the PAC Compressor in PTA-5/6.
  Find which factors affecting PAC compressor efficiency and how we can resolve it.
  What are the major causes of efficiency losses in the PAC system.
  Impact of suction conditions, cooling efficiency, and pressure drops on overall efficiency as well as Weather.
  Recommendations for improving PAC compressor performance and operational reliability.

## Slide 26
Recommendation
  Ensure proper installation, alignment, and handling of air seal strips during maintenance and shutdown activities to prevent damage and air bypassing.
  Carry out periodic cleaning and inspection of finned tube bundles to maintain effective heat transfer performance.
  Monitor intercooler outlet temperature, pressure drop, and condensate generation regularly to detect performance deterioration at an early stage.
  Maintain adequate cooling water flow and quality to minimize fouling and sustain intercooler effectiveness.
  Conduct periodic compressor performance audits to identify efficiency losses and implement corrective actions proactively.
  Adopt a condition-based maintenance approach for intercoolers and compressor internals to prevent unexpected failures and efficiency degradation.